## Slide 1: High Speed LVDS Receiver Design
In LBC9 Technology Node
Aniket Sen, Analog Intern

## Slide 2: Key Specifications
 | Min. | Typ. | Max.
Common Mode Range | -1V | -- | 3.4V
Supply Voltage | 3.0 | 3.3 | 3.6
Maximum Operating Frequency | 250MHz (500Mbps) |  | 
Ambient Temperature | -40º C | -- | 150º C
Input Differential Voltage (¦VID ¦) | 100mV | 200mV | 400mV
Leakage Current in Bus |  |  | 2
 | Min. | Typ. | Max.
Common Mode Range | -1V | -- | 3.4V
Supply Voltage | 3.0 | 3.3 | 3.6
Maximum Operating Frequency | 250MHz (500Mbps) |  | 
Ambient Temperature | -40º C | -- | 150º C
Input Differential Voltage (¦VID ¦) | 100mV | 200mV | 400mV
Leakage Current in Bus |  |  | 
Typical common mode voltage for LVDS transmitter output is 1.2V but there is a ground variation of 2V that is considered between transmitter and receiver

## Slide 3: Existing LVDS Receiver Architecture
Attenuator Stage
Rx Comparator
Outer Buffer
Differential signal from Transmitter
Low Gain Stage
High Gain Stage
Latch
Circuit
In LBC7 technology node
Differential Rail-to-Rail Output

## Slide 4: Attenuator Block Diagram
Bus
= (
= (
This is the common mode attenuation that we want from the block
The differential signal also gets attenuated

## Slide 5: Why we require Attenuator Block ?
There is a restriction in the input DC voltage of the low gain amplifier block so that all the transistors are in saturation. So, we attenuate the input signal first to the desired range.
How to choose the value of R1 and R2 ?
If we know the attenuation required, we would get the value of R1 / R2 . To uniquely choose the values, we would get from the leakage current specs as the input signal to the attenuator block is directly connected to the bus channel.
Leakage Current in the bus < 2
Thus,
So, R1 and R2 would be of order

## Slide 6: Low Gain GmR Stage
I
I
I/2
R
R
Vs
Vd
Differential Input
( VCM )
Differential Output
To maintain the I/2, if we decrease our gate voltage of M2 , then the source Vs would also decrease to make VGS constant of M2 . Thus, there we get a lower limit on our input voltage.
Also, if we keep increasing our gate voltage of M2 , then after a certain increase, the condition of saturation gets failed : VDS > VGS – Vtn as the Vd is fixed due to constant current.
< VCM <
M1
M2
M3
Gain =

## Slide 7: Effect of Attenuation and Gain
To increase gain, if we increase the IR, then the attenuation would decrease and maybe we won’t get the desired range. So, to optimize that we want the max of the product of attenuated range and the Gain :
Product = (
= ( 1.6 – 0.3 – 0.3 - ) * = (1 - ) *
This product gets maximum at IR = 2
Choosing higher current will lead to a better rise time but would dissipate more power.
This is a quadratic in IR !

## Slide 8: Problems of Attenuation Block
Too much RC compensation required for flattening out the frequency response.
Node capacitors are large due to high resistances used making the circuit slow.
Differential Signal also gets attenuated along with the common-mode.
This motivates to work on a new input stage architecture for receiver block that could skip the attenuator thing !
Attenuation Block

## Slide 9: Common Gate Architecture Design
To track VGS and pushes constant current through the common gate design
Vin1
Vin2
Vin1
Vin2
Vdd
I
R1
R1
Input is given directly at the Gate to make VGS > Vtn for negative common mode also
The reason of diode connection would be to mirror the current which would be explained later why.
There is an error here !
To get the DC common mode
We will not get DC common mode as there would be an I/2 current in R1 branch that would be contributing some more potential.

## Slide 10: Common Gate Architecture Design
R1
R1
R2
R2
I
nI
nI
I/2
I/2
Vin1
Vin2
Vin1
Vin2
Fixing the error by adding an extra resistor R2 to raise the source voltage.
Equating the potentials :
Vin1 + IR1/2 = Vin1 + nIR2/2
IR1 = nIR2
R1 = nR2

## Slide 11: Common Gate Architecture Design
R1
R1
R2
R2
I
nI
nI
I/2
I/2
Vin1
Vin2
Vin1
Vin2
This voltage is fixed !
Gate voltage keep rising as common mode input increases
Thus, there is an upper bound to this design !

## Slide 12: Common Gate Architecture Design
R1
R1
R2
R2
I
nI
nI
I/2
I/2
Vin1
Vin2
Vin1
Vin2
M1
M2
M3
M4
M5
VCM < VDD - |Vtp|- Vov|M4 - Vov|M5
This we would control and try to make it as small as possible
Now, apply similar architecture for high common mode voltage in its input

## Slide 13: Common Gate Architecture Design
I
nI
nI
R2
R2
R1
R1
M1
M4
M5
M2
M3
Vin1
Vin2
Vin2
Vin1
I/2
I/2
This would work for higher common mode voltages.
The limit is
VCM > Vov|M2 + Vov|M4 + IR/2 + Vtn
This we would control and try to make it as small as possible

## Slide 14: Common Gate Architecture Design
The NMOS based design
The PMOS based design
R1
R1
R2
R2
Current will be mirrored to Max current Selector Block
Current will be mirrored to Max current Selector Block

## Slide 15: Max Current Selector Block
RL
Ip
IN
IN1
M1
M2
M3
M4
M5
Case 1 : IN > IP
The drain of M5 is pulled up to VDD such that the current from M3 drops to zero and the M2 goes to linear region and matches Ip . Thus, total current in load branch = 0 + IN = IN = max(IP , IN)
Case 2 : IN < IP
Then IN1 = IN and remaining (IP – IN) flows from the transistor M3 which is mirrored to the M4 branch. Thus, total current from load is (IP – IN) + IN = IP = max ( IP , IN )
Case 3 : IN = IP
Then no current flows from M3 branch and again current from load branch is IN which is max of (IN , IP ).
Maximum of IN and IP flows through the load RL
Fig. Max Current Selector Block

## Slide 16: Common Gate Architecture Design
This is being mirrored from the PMOS-based common gate
This is being mirrored from the NMOS-based common gate
Thus, the motive behind this block is to send the maximum current between the PMOS based and NMOS based common gate design which would be a constant current “nI” through the load covering the wide common-mode range.
RL

## Slide 17: Common Gate Architecture Design
RL
IP1
IN1
M11
M12
M13
M14
M15
RL
IP2
IN2
M16
M17
M18
M19
M20
R1
R1
R2
R2
VDD
VDD
IN1
IN2
IP1
IP2
VDD
Vout1
Vout2
Vin2
Vin2
Vin1
Vin1
New Architecture of Input Stage of High Speed LVDS Receiver Design
M3
M4
M5
M6
M10
M9
M8
M7
M2
M1

## Slide 18: Body Connection
For removing the non-linearity of body-effect, we tied the body locally to its source. But, the negative voltage was creating some problem.
P-epi
ISO
For D3 to be reverse biased, ISO could be grounded or make to it AVDD
D1
D2
D3
For D1 to be reverse biased, we try to bias p-epi to ground but at negative common-mode voltages, the diode D1 would become forward biased.
Fig. Current leakage from body in PMOS

## Slide 19: FIXATION OF THE ISSUE
D1
D2
D3
Now, D1 is reverse-biased
Just ensure D2 and D3 to be reverse biased and that could be pretty much done by either making ISO to AVDD or GND
SOLUTION :
Short the Body and drain to the p-epi node for not having any path for the current to flow.
Remember, the objective was to get a flat gain across VCM which motivated to nullify the body-source effect.

## Slide 20: AC Gain
For lower VCM :
Gain =
For VCM ~ 1.5V :
Gain =
For higher VCM :
Gain =
Gain
VCM
-1V
3.4V
1.5V
This drop could be removed if gM5R2 + gM9R2 <<1
Design such that gM5 = gM9 for same gain at the corners

## Slide 21: Frequency Response
RL
IP1
IN1
M11
M12
M13
M14
M15
RL
IP2
IN2
M16
M17
M18
M19
M20
R1
R1
R2
R2
VDD
VDD
IN1
IN2
IP1
IP2
VDD
Vout1
Vout2
Vin2
Vin2
Vin1
M3
M4
M5
M6
M10
M9
M8
M7
M2
M1

## Slide 22
THANKS